## Slide 1: EDPR Journal Club
VOR Adaptation on a Humanoid iCub Robot Using a Spiking Cerebellar Model

## Slide 2: Abstract
Spiking Cerebellar Model (Event-Driven, Neurons, STDP)
  Different Neural Activity leads to different computation times
  Two-stage learning process
Adaptive real-time (RT) control loop
  RT Supervisor changes cerebellar simulation dynamically
  Biological sensory motor delay
Operating a Real Robotic Body (iCub)
Different VOR Tasks (horizontal and vertical)

## Slide 3: Introduction
Embodied Cognition = Aim of Central Nervous System is to control a Body in a real Environment
Cerebellum manages muscle control (Coordination, Precision, Timing)
Cerebellum manages VOR (Vestibulo-Ocular Reflex)

## Slide 4
Notes: VOR Aim=> Stabilize Images on the Fovea (sharp field on the Retina)
r-VOR = rotational VOR
t-VOR = translational VOR
How: Cerebellum produces opposite Eye movements as in left figure
Right Figure: Interplay of rotations
Phase and Gain are values to measure Performance of Compensation

## Slide 5
(b)
Notes: Control loop
  Reference Var = Head Velocity (t)
  Feed forward = computation in one direction -> no direct feedback
  VOR Plant model = Sensory Motor Delay
  Controlled Var = Eye Velocity (t)
  Retinal Slip (t)(=Error) = Head Velocity(t) – Eye Velocity (t)
Cerebellar Connectome Diagram:
  Sensory Info Head -> Semi-circular Canals -> Mossy Fibers excite -> Granular Cells
                -> Vestibular Nuclei
  Granular Cells excite -> Purkinje Cells inhibit-> Vestibular Nuclei excite -> Oculomotor Nucleus drives -> Eye muscles
  Sensory Info Eyes -> Accessory optic system -> Inferior Olive calculates Error and excites via Climbing Fibers -> Purkinje Cells and Vestibular Nuclei

## Slide 6: Introduction
Biological study difficult -> Computational Simulation and compare to Biology
VOR Setup:
  VOR Task -> well-defined motion of the head, where we can compare the data to humans
  Cerebellar spiking model -> feed-forward controller
  Humanoid Robot -> operate iCub in RT

## Slide 7: Material and Methods
B. Cerebellar Neural Network
5 Neural Subpopulations (MF, GC, PC, VN, IO)
Simulator = EDLUT (Simulator made by Authors for RT Experiments)
Notes: EDLUT = “Event-Driven simulation scheme using lookup tables to characterize neuronal dynamics”

## Slide 8
Notes: 100 Mossy Fibers -> Input Neurons/ ”parrot neurons”
2000 Granular Cells -> “State Generator” generates spatio-temporal patterns
200 Purkinje Cells -> 100 Agonist -> Single Compartment Hodgkin-Huxley Model with 3 spike modes
-> 100 Antagonist
200 Inferior Olive -> 100 Agonist -> LIF + Intraconnections + Poisson Process (Error > random number between 0 and 1, meaning high errors are more likely to spike) -> 100 Antagonist
200 Vestibular Nuclei -> 100 Agonist -> LIF -> VN-Output = correction (Velocity/Spikes) * (sum(Agonist) – sum(Antagonist))(Spikes)
-> 100 Antagonist

## Slide 9: C. Spiking Neuron Models
LIF (VN)
Notes: g_l = leak current (decay)
Decay * (Membrane Potential + Resting potential) = Internal Current
-(Current(AMPA) + Current(NMDA)*Current(NMDA_INF)) * (Membrane Potential – Resting Potential(AMPA) – Current(GABA) * (Membrane Potential – Resting Potential(GABA)) = External Current

## Slide 10: C. Spiking Neuron Models
LIF (IO)

## Slide 11: C. Spiking Neuron Models
HH (PC)
Notes: g_m is special, because it decays slower than all the other currents and enables three different states: “burst, silence and tonic”

## Slide 12: D. Synaptic Plasticity
Spike-Timing Dependent Plasticity (=STDP)
LTP (= Long-Term Potentiation)

## Slide 13: D. Synaptic Plasticity
Spike-Timing Dependent Plasticity (=STDP)
LTD (= Long-Term Depression)

## Slide 14: D. Synaptic Plasticity
Competition of LTP to LTD

## Slide 15: D. Synaptic Plasticity

## Slide 16: D. Synaptic Plasticity

## Slide 17: E. VOR Plant
Total biological sensorimotor pathway delay is modelled in EDLUT using:
E(s) = eye motion (Output)
H(s) = head motion (Input)
k = gain parameter [0.6 ; 1]
Tc1 = canals setback + neural processing [10; 30] [s]
Tc2 = oculomotor delay [0.005 ; 0.05] [s]
tdelay = synaptic delay [0.005] [s]
Notes: Tc1 = 15s

## Slide 18: F. iCub Robot
Simulated iCub in Gazebo: iCub_SIM
Real iCub controlled with YARP (only control neck, eyes and cameras)

## Slide 19: G. Control loop

## Slide 20: G. Control Loop
Simulation Time Cerebellum (=cerebellar internal clock)
Simulation Time Robot (= iCub internal clock)
technological delay (=15 ms)
Biological delay (= 100 ms)

## Slide 21: H. Real Time Supervisor
PC Layer -> Time-Driven, high Activity
GC Layer -> Event-Driven, sparse Activity
Optimization of , but nondeterministic
Therefore need for RT Supervisor

## Slide 23: I. Experimental Protocol for Cerebellar Validation
Rotatory Chair Test (Head restrained, Frequency [0.5 - 5Hz])
Eyes follow stationary target -> VOR
Test Subjects: iCub vs. Monkey

## Slide 24
Notes: Gain = Peak eye velocity / Peak Head Velocity = 1
Phase = Lag between Head and Eye Velocity = 180°
 Robot is doing better job than the monkey in following these parameters

## Slide 25: Results
A. Cerebellar Adaptation Process
Notes: Experiment with Frequency = 1 Hz, Velocity = 150 °/s:
Starting with initial learning stage above:
X-Axis = Simulationtime [in s]
Y-Axis_up = Neuron ID
Y-Axis_down = Velocity [°/s]
Violet color = GC Population (from 100-2099)
Crème color = MF Population ( from 0-99)
MF activity down graph: Zoom shows each 4 MF are coding for one velocity
GC activity up graph: Following Sinusoid Head Movement down
Error: First Antagonist, then Agonist fires
Output VN: No signal, because maximally inhibited by PC
Ending with final learning stage:
Head Signal stays the same, but Error Signal and VN Output changed

## Slide 26: Two learning stages
Notes: Two plots showing the two learning stages of STDP mechanisms:
r-VOR Task, Velocity = 150 °/s, Frequency = 1 Hz
Above PF-PC synaptic weights and down MF-VN synaptic weights
PF-PC:
X-Axis: PF from 0-2000
Y-Axis: PC from 0-200
All-To-All-Connection
Legend: dark blue: 0 nS -> no weight
Yellow: 4 nS -> initial weight (should range to 10 according to table before)
Sinusoid pattern, because GC(PF) shoot at the PC in that pattern, which means highest activity during the changing points of the sinusoid motion
MF-VN is the photo negative of the PF-PC, because when PC shoots, the LTD mechanism at MF shoot as well!

## Slide 27
Notes: Mean Absolute Error Evolution:
MAE always maximal in the beginning, decreasing during the Cerebellar Adaptation until STDP mechanisms are fully established
The larger the Head Velocity amplitude to compensate, the greater the VN output and the longer it takes to obtain optimal weights

## Slide 28: B. Meeting RT Requirements and RT Supervisor Process
Notes: a) Left up: Horizontal r-VOR Task, 150 °/s, simulated iCub:
RT Supervisor makes STnet = RT,
Without STnet < RT, meaning the robot does not get the information at the right time
b) Left down: Simulation time distance < 85 ms; changes during two seconds of trial about 500 ms without RT Supervisor
c) Right up: Around 85 ms, colors indicate contingency levels
d) Right down: Contingency levels

## Slide 29
Notes: Around 98.69% of 300s, the STnet is standard
1.31% the Simulation gets degredated
How does this affect the simulation:
Looking at the difference of STDP weight distribution and MAE evolution between RT and noRT

## Slide 30: C. Robotic r-VOR Cerebellar Adaptation (Proof of concept)
Movies with simulated and real iCub
Optical flow computed over camera images
Quantitative indication of image stabilization with red (right, down) and green (left, up)

## Slide 31: Discussion
Machine learning family:
  Biologically inspired but not biologically plausible
  Aim is to solve VOR Task
  Examples: Supervised NN, Adaptive Filters, LWPR
Cerebellar-based family:
  Biologically inspired and plausible
  Aim is to understand cerebellar primitives
  Examples: Analog Cerebellar Models (computational efficient and easy RT)
  Spiking Cerebellar Models (computational heavy and hard RT)

## Slide 32: Conclusion
What is new: Operating Real Robot in Real Time
Inner/Outer Control Loop
RT Supervisor